## Slide 1: A Programmable Multi-Channel Sub-Threshold FIR Filter for a Body Sensor Node
Alicia Klinefelter
Dept. of Electrical Engineering, University of Virginia
January 16, 2012

## Slide 2: Motivation
Wireless body sensor nodes (BSN) well-suited for sub-threshold
Accelerators more energy efficient than MCU
  No multiplier on MCU
  Filtering operation frequently used
Application: EEG signal power extracted from multiple frequency bands
  Prior work used analog multi-channel FIR for energy extraction [4]
A need for filtering flexibility
Portability

## Slide 3: Outline
Design Overview
  Context: Full chip
  FIR Overview
Filter Decisions and Tradeoffs
  Filter topologies
  Filter and Channel Design
  Leakage Reduction
Filter Features
Results
  Design Comparison
Future Work

## Slide 4: BSN Overview
19µW chip including analog front-end (AFE), memory, digital processing, power management and TX
Ultra-low power:
  Batteryless
  Harvested energy
FIR part of flexible data path.
BSN Node Chip Micrograph [3]
BSN Node Datapath Flexibility [3]

## Slide 5: FIR Overview
Configurable/Programmable
  Number of taps
  Number of filters
  Coefficients
Four input and processing channels
Synthesized and fabricated in a 130nm technology using the Cadence design flow:
  Verilog  RC Compiler  Encounter Place and Route  Virtuoso
Operates down to 300mV at 8kHz
Employs clock and power gating for energy savings

## Slide 6: Outline
Design Overview
  Context: Full chip
  FIR Overview
Filter Decisions and Tradeoffs
  Filter topologies
  Filter and Channel Design
  Leakage Reduction
Filter Features
Results
  Design Comparison
Future Work

## Slide 7: Architectures for Low Power: IIRs
Infinite impulse response (IIR): fewer taps, sharper cutoff
Non-linear phase tolerable for application
Instability a big problem

## Slide 8: IIR: Instability
Desired cutoff results in poles near unit circle

## Slide 9: Architectures for Low Power: FIR
Direct form FIR
More coefficients to achieve desired cutoff
  Symmetric coefficients
No feedback  No stability problems

## Slide 10: Channel Design
Resource-shared architecture [2]
  1 adder, 1 multiplier per channel
1 tap computed per clock cycle
  195-781 fast clock cycles per sample clock period
Channel control logic
  Maintains channel state
  Clock gating control
b0
b0x[n]
x[n]
0
y[n] = b0x[n]
x[n-1]
b1
b1x[n-1]
b0x[n]
y[n] = b0x[n]+b1x[n-1]
fast clock
. . .
x[n-k]
bk
bkx[n-k]
b0x[n]+…+
bk-1x[n-k-1]
y[n] = b0x[n]+…+bkx[n-k]
sample clock

## Slide 11: FIR Block Diagram

## Slide 12: Sleep Mode Power Savings
Power gating
  For when block is not on the datapath
  Simulated power gated channels
Clock gating
  Many fast clock cycles not used per sample period
  Clock gate all channels after result computed or block is off

## Slide 13: Outline
Design Overview
  Context: Full chip
  FIR Overview
Filter Decisions and Tradeoffs
  Filter topologies
  Filter and Channel Design
  Leakage Reduction
Filter Flexibilty
Results
  Design Comparison
Future Work

## Slide 14: Features: Taps Selection
Prior works has 8-14 taps
E/sample increases with more taps
Throughput still met with more clock cycles
Notes: Normalized frequency axis is the passband normalized to the Nyquist frequency (sampling rate / 2)

## Slide 15: Features: Number of Taps
Programmable number of taps
  Half taps mode (15 taps) for less accurate results
  Full taps (30 taps) for a more accurate result
  Can use adder on chip’s CPU to create 60 tap filter
Programmable number of filters
Notes: Half-taps mode: if battery energy on chip is low, you can output lower quality results

## Slide 16: Outline
Design Overview
  Context: Full chip
  FIR Overview
Filter Decisions and Tradeoffs
  Filter topologies
  Filter and Channel Design
  Leakage Reduction
Filter Features
Results
  Design Comparison
Future Work

## Slide 17: Results: Frequency Response
(a)
(b)
(c)
(d)
Measured frequency response for varying tap lengths (a) 18-12Hz (b) 18-26Hz (c) 30-50Hz (d) 70-100Hz
Notes: Add ED curve for 4 channels, and then half taps for 1 and 4 channels

## Slide 18: Measured Results: ED Curve
350mV, 28kHz
350mV, 22kHz
Notes: Add ED curve for 4 channels, and then half taps for 1 and 4 channels

## Slide 19: Measured Results: EEG Filtering
time(s)
Voltage (V)
(a)
(b)
(c)
(d)
(e)
Filtering of EEG data set. (a) Original signal sampled at 250Hz (b) filtered at 8-12Hz (c) filtered at 18-26Hz (d) filtered at 30-50Hz (e) filtered at 70-100Hz
*data from [1]
f (Hz)
|Y(f)|
Notes: Add ED curve for 4 channels, and then half taps for 1 and 4 channels

## Slide 20: Design Comparison
 | This Work | [5] | [6] | [4]
Type | 30-tap, 8-bit | 8-tap, 8-bit | 14-tap, 8-bit | 4th order analog
Channels | 4 | 1 | 1 | 4
Programmable | a | r | r | a
Technology | 0.13μm | 0.13μm | 0.13μm | 0.13μm
Supply | 0.4V | 0.2V | 0.27V | 1.2V
Frequency | 100kHz | 12kHz | 20MHz | 20kHz
Power | 118nW | 114nW | 310μW | 780nW
Energy | 1.18pJ | 9.5pJ | 15.57pJ | 39pJ
FOM* | 0.61 | 18.55 | 17.37 | N/A
*FIR FOM: power(nW)/frequency(MHz)/# of taps/input bit length/coefficient bit length

## Slide 21: Outline
Design Overview
  Context: Full chip
  FIR Overview
Filter Decisions and Tradeoffs
  Filter topologies
  Filter and Channel Design
  Leakage Reduction
Filter Features
Results
  Design Comparison
Future Work

## Slide 22: Future Work
Fine-grained power gating analysis
Programmable number of taps: any number
Increased Channel flexibility
  Process all 4 channels in parallel
Dynamic programming options
Reduce register overhead through use of latches or data memory
CH0
CH2
CH3
CH1

## Slide 23: References
R. Leeb, , C. Brunner, G. R. Muller-Putz, A. Schlogl, and G. Pfurtscheller. “BCI Competition 2008 - Graz data set B 1”. Institute for Knowledge Discovery, Graz University of Technology, Austria, Institute for Human-Computer Interfaces, Graz University of Technology, Austria.
Davis, W.R. , et al., "A design environment for high throughput, low power dedicated signal processing systems," Custom Integrated Circuits, 2001, IEEE Conference on , 2001.
Fan Zhang, et al., "A Batteryless 19μW MICS/ISM-Band Energy Harvesting Body Area Sensor Node SoC," International Solid-State Circuits Conference (ISSCC), 2012 IEEE , Feb. 2012.
Fan Zhang, et al., "A low-power multi-band ECoG/EEG interface IC, “Custom Integrated Circuits Conference (CICC), 2010 IEEE , Sept. 2010.
Myeong-Eun Hwang, et al., “A 85mV 40nW Process-Tolerant Subthreshold 8x8 FIR Filter in 130nm Technology," VLSI Circuits, 2007 IEEE Symposium on , June 2007.
Wei-Hsiang Ma, et al., "187 MHz Subthreshold-Supply Charge-Recovery FIR," Solid-State Circuits, IEEE Journal of , April 2010.

## Slide 24: Thank You Questions?